## Slide 1: Chemical Hygiene Plan/Laboratory Safety Training
Occupational Health and Safety
Notes: Welcome to the Chemical Hygiene Plan/Laboratory Safety Training Class. This class is presented by Occupational Health and Safety. This class is a mandatory class for all laboratory personnel.

## Slide 2: Table of Contents
Introduction
Responsibilities
Standard Operating Procedures/Standard Practices
Controlling Chemical Exposures
Chemical Fume Hoods and Other Engineering Controls
Employee Information and Training
Prior Approval
Medical Consultation
Special Provisions for Select Carcinogens, Reproductive Toxins and Toxic Chemicals
Notes: This training will cover the basic information needed to be in the lab safely.

## Slide 3: Introduction
The Chemical Hygiene Plan is part of the University’s compliance with the regulations promulgated on Jan. 31. 1990 by the U.S. Department of Labor Occupational Health and Safety Administration (OSHA).
This Standard entitled, “Occupational Exposures to Hazardous Chemicals in Laboratories” is hereafter referred to as the Lab Standard.
Notes: The standard that regulates the laboratory is titled, “Occupational Exposures to Hazardous Chemicals in Laboratories” This is generally known as the lab standard and was put into law by OSHA in 1990.

## Slide 4: Responsibilities of Chemical Hygiene Plan
Standard Operating Procedures
Criteria to determine and implement specific control measures, such as engineering controls and personal protective equipment
A program that ensures that fume hoods and other engineering controls are functioning properly
Information and training requirements
When a lab will require “prior approval”
Provisions for medical consultation and medical exams
Designation of the Chemical Hygiene Officer
Additional precautions for select carcinogens, reproductive toxins and extremely toxic substances.
Notes: The purpose of this model Chemical Hygiene Plan (CHP) is to define work practices and procedures to help ensure that laboratory workers at the University of Kentucky are protected from health and safety hazards associated with hazardous chemicals with which they work.

## Slide 5: Covered by standard
Everyone is covered by the standard that works in a laboratory.
Laboratory is defined by OSHA as, “a workplace where relatively small quantities of hazardous chemicals are used on a non-production basis.”
Laboratory workers should be 18 years or older. For students age 17 and under, prior approval is needed through the Minors in Lab Policy
Notes: All personnel that work in a lab are covered by this standard. The standard defines a laboratory as “a workplace where relatively small quantities of hazaroud chemical sare used on a non-production basis.” A lab is also considered a place where chemicals are easily handled and manipulated by a person. All laboratory workers must be 18 years of age. If a laboratory plans to have a laboratory worker age 17 or younger then prior approval through the Occupational Health and Safety Department is needed.

## Slide 6: Training Requirements
Before commencement of lab duties, all laboratory workers must read the Chemical Hygiene Plan.
Training records should be kept with either the Principal Investigator (PI) or the lab supervisor.
The chemical Hygiene Plan must be reviewed annually by the Laboratory’s Chemical Hygiene Officer and the “revised date” must be listed on the identification page.
Notes: All personnel must read the Chemical Hygiene Plan before work may begin. The training records for the laboratory personnel must be kept with the Supervisor or PI. Annually the Chemical Hygiene Plan must be reviewed. The revision date should be listed on the ID page.

## Slide 7: Training Requirements continued
At a minimum, the following classes must be taken for ALL laboratory personnel.
  Chemical Hygiene Plan/Laboratory Safety
  Chemical Hygiene Plan Annual Refresher
  Hazardous Waste
  Fire Extinguisher Training
If other hazards are present in the lab, such as biological or radiological agents, training must be conducted in these areas as well. Below is a link to Environmental Health and Safety Training Checklist
Notes: All laboratory must take the following classes when working in the laboratory. The Chemical hygiene plan/laboratory Safety. This training that is being taken now, meets this requirement. This training is only required once. The Chemical Hygiene Plan Annual Refresher is a shorter version of the Chemical Hygiene Plan/ Laboratory Safety and will need to be taken annually.
Hazrdous Waste and Fire ext. Training are classes offered online that are also required annually.

## Slide 8: Responsibilities associated with Laboratory Safety and the Chemical Hygiene Plan
Environmental Health and Safety Department’s Responsibilities
  Appoint an Institutional Chemical Hygiene Officer who will routinely review the model Chemical Hygiene Plan and suggest modifications as needed
  Provide technical assistance to Laboratory Supervisors and workers concerning appropriate storage, handling and disposal of hazardous chemicals
  Provide general laboratory safety training upon request
  Conduct exposure assessments and laboratory inspections upon request and on a routine basis
  Provide technical assistance concerning personal protective equipment and laboratory safety equipment
  Remain current on rules and regulations concerning chemicals used on campus
Notes: The University of Kentucky is committed to providing a safe and healthful environment for all person associated with the institution.

## Slide 9: Responsibilities of Deans, Directors and Heads of Academic and Administrative Units
Collaborate with faculty and staff to adapt the Model Chemical Hygiene Plan to include lab-specific guidelines and to develop strategies to implement the Plan
Consider the idea of developing departmental-wide laboratory safety training programs and/or committees
Make budget arrangements for health and safety improvements. It is the responsibility of these respective individuals to request the necessary monies in the budget process
Notes: Deans, Directors and Heads of Academic and Administrative Units have the primary responsibility for the health and safety of their staff and students. Specific responsibilities regarding the implementation of the Chemical Hygiene Plan includes:

## Slide 10: Responsibilities of Faculty and Staff
Inform and train employees concerning chemical safety as required by this Plan. Retain training records and all documentation.
Implement and enforce rules and standard of this plan concerning health and safety for laboratories under the supervisor’s jurisdiction and restrict access to the laboratory
Serve as the Chemical Hygiene Officer for the laboratory
Ensure compliance of laboratory workers in the Plan
Notes: Faculty and staff in charge of supervising laboratories (referred to as Laboratory Supervisors throughout document) have the following responsibilities for implementing the Chemical Hygiene Plan:

## Slide 11: Faculty and Staff Responsibilities continued
Ensure the availability and enforce the proper use of appropriate personal protective equipment and relevant health and safety reference materials
Remain cognizant of chemicals stored and used in labs and their associated hazards
Develop an annual inventory of chemicals present in the laboratory (E-trax electronic system)
Conduct internal inspections for health and safety concerns and maintain an inspection log
Request assistance from Environmental Health and Safety, as needed
Request allocation of funds from superiors for health and safety improvements

## Slide 12: Laboratory Worker Responsibilities
Follow all health and safety standards and rules
Report all hazardous conditions to the laboratory supervisor
Wear or use prescribed protective equipment
Report any suspected job-related injuries or illnesses to the laboratory supervisor and seek treatment immediately
Refrain from the operation of any equipment or instrumentation without proper instruction and authorization
Remain aware of the hazards of the chemicals in the lab and how to handle hazardous chemical safely
Request information and training when unsure how to handle a hazardous chemical or procedure

## Slide 13: Standard Operating Procedures (SOPs)

## Slide 14: Standard Operating Procedures/ General Practices
The Lab Standard requires operating procedures relevant to safety and health consideration to be followed when laboratory work involves the use of hazardous chemicals.
Notes: This Plan represents a minimum set of guidelines for the handling of hazardous chemicals in laboratories at the University of Kentucky. Individual administrative units, laboratories or research groups are required to develop more detailed procedures as their situations warrant. These procedures must be written, added to the laboratory's Chemical Hygiene Plan, and made available to Laboratory Workers. Acceptable lab safety references such as those listed in the Forms section may be adopted in whole or may be useful in developing additional procedures. In all situations, individual faculty or staff will be responsible for enforcing adequate safety and hygiene measures in laboratories they supervise. If necessary, additional assistance from Environmental Health and Safety is available. A table of violations can be used as a guide for enforcing the adequate safety and hygiene measures. The following standard operating procedures apply to all labs at UK:

## Slide 15: General SOPs/Standard Practices
Authorized Access – The Laboratory Supervisor must restrict access to laboratories. Children (under age 17) are not allowed in the laboratories except as authorized by the Laboratory Supervisor for an officially sanctioned activity (e.g. class or open house or approved Minor’s in lab form). Pets are also prohibited from laboratories.
Containers - Check the integrity of containers and if damaged or leaking, transfer to an acceptable container or call Environmental Management for assistance (323-6280). For disposal, submit an E-trax electronic ticket to Environmental Management. Observe compatibility; for example, hydrofluoric acid must not be stored in glass and some oxidizers should not be stored in plastic containers.
Notes: Respect and understand the safety and health hazards associated with the chemicals and equipment in your laboratory, and practice the following general safety guidelines at ALL times:

## Slide 16: General SOPs/Standard Practices
Compressed Gas Cylinder Handling--Use appropriate handcarts to move cylinders. Cylinders must be secured at all times. Extremely toxic gases (e.g. hydrogen sulfide, chlorine, arsine) should not be moved through regular exit corridors, particularly during business hours. Always consider cylinders as full and handle them with corresponding care. NOTE: For additional information on cylinder handling, go to the Compressed Gas Cylinders Guide.

## Slide 17: General SOPs/Standard Practices
Door View Panel – Lab view panels should not be covered.
Equipment –Use proper equipment that is in good condition. For example, never use chipped or cracked glassware. Shield pressurized or vacuum apparatus and safeguard against bumping or overheating.
Glass Tubing –When inserting tubing into stoppers, lubricating tubing as well as wearing gloves or wrapping in a thick cloth will help protect hands from being cut in the event of the tubing slipping and breaking.
Notes: A door view panel should not be obstructive. Equipment should be in good condition.

## Slide 18: General SOPs/Standard Practices
Disposal of Waste – It is important to segregate wastes. To request pick-up of hazardous waste, biohazardous waste or chemicals, fill out an E-trax electronic ticket. Disposal of all laboratory waste must follow the procedures specified by Environmental Management (323-6280). To request pick-up of radioactive wastes, contact Radiation Safety at 323-6780.

## Slide 19: General SOPs/Standard Practices
Food, Drink, Cosmetics. Eating, drinking and the application of cosmetics (including lip balm) is forbidden in areas where hazardous chemicals are used and must be done only in well-defined designated non-chemical areas. Do not store food in the same refrigerator with chemicals, biohazards or radioactive materials. Refrigerators, microwaves and ice machines must have labels that denote their use, i.e. "Not for food or drink”

## Slide 20: General SOPs/Standard Practices
Hazardous Materials – Hazardous materials should not be used on open laboratory benches.
Horseplay – Horseplay, practical jokes or other inappropriate and unprofessional behavior in the laboratory setting is forbidden. Avoid distracting or startling other workers.
Housekeeping – Exits, aisles and safety equipment must NOT be obstructed in any way with equipment, furniture, etc. No items must be stored in the corridors. For questions related to the use of corridors or any exiting or Fire Marshal issue, contact the Fire Marshal (257-8590).
Notes: Hazardous materials should never be used on the laboratory benches.

## Slide 21: General SOPs/Standard Practices
Mercaptans –To avoid false reporting of natural gas leaks, the Physical Plant department should be contacted when mercaptans are used in a laboratory in such a manner that persons outside of the laboratory could smell the mercaptan and suspect a natural gas leak in the building. For more information about mercaptans please see the fact sheet .

## Slide 22: General Sops/Standard Practices
Mouth Pipetting –Mouth pipetting is forbidden.
Natural Gas –The Natural Gas Emergency Response Procedures are designed to provide a structured means for safe evacuation and notification of affected personnel when a potential Natural Gas Emergency exists. For more information please see the natural gas fact sheet.

## Slide 23: General SOPs/Standard Practices
No Smoking. –This policy exists throughout the University and applies in all laboratories.
Perchloric Acid –If perchloric acid is heated above ambient temperature it will give off vapors that can condense and form explosive perchlorate salts. Hence, when heating perchloric acid above ambient temperature, a specifically designed and dedicated perchloric acid fume hood with a wash down system or a local scrubbing or trapping system must be used.

## Slide 24: General SOPs/Standard Practices
Unattended Experiments –Frequently, laboratory operations are carried out continuously or overnight. For experiments involving hazardous operations, it is essential to plan for interruptions in utility services such as electricity, water and inert gas. Operations are to be safe and plans made to avoid hazards in case of failure. If necessary, arrangements for routine inspection of the operation are to be made and, in all cases, the laboratory lights should be left on and an appropriate sign posted on the door.

## Slide 25: General SOPs/Standard Practices
Working Alone –When working with acutely hazardous materials, it is advisable to have a second person present, or at a minimum, maintain surveillance via telephone contact.

## Slide 26: Personal Standard Operating Procedures

## Slide 27: Personal Protective Equipment.
OSHA has amended standards for personal protective equipment (PPE) to require employers to assess the workplace to determine if there are hazards requiring the use of PPE and certify that this assessment was performed. The following generic PPE requirement for labs can be used and supplemented as appropriate. For additional hazards, contact Occupational Health and Safety Department, 7-3827.

## Slide 28: Personal Attire
Personal protection and personal hygiene are two very basic aspects of laboratory safety. Wearing appropriate personal protective equipment and practicing good personal hygiene as described below will minimize exposures to hazardous chemicals during routine use and in the event of an accident.

## Slide 29: Personal Protective equipment (PPE)
Attire –Wear a lab coat or apron, cover legs and feet (no sandals or open-toed shoes), and confine loose clothing and long hair. For addition information see the PPE& Apparel In Chemical Labs Fact Sheet

## Slide 30: PPE
Gloves- Gloves are essential when working with hazardous substances. The proper gloves will prevent skin absorption, infection or burns. All gloves materials are not equally effective in protection from chemical hazards. Consult a chemical resistance chart such as the one found in the Glove selection guide, or consult a glove manufacturer. Environmental Management (323-6280) and Occupational Health and Safety (257-3827) are also available to assist with glove selection.

## Slide 31: PPE
Eye Protection –It is University of Kentucky policy that personnel including students, staff, and visitors in laboratories wear appropriate safety glasses, goggles or face shields at all times, when chemicals are stored or handled. Goggles are required when chemical splashes are possible.
Face Shields –Full Face shields must be worn when conducting a procedure where splashing is a potential. Full face shields with bottom caps to protect under the chin are preferred due to the tendency to raise the chin when a splash occurs.

## Slide 32: PPE Assessment Guide
HAZARD ASSESSMENT AND PERSONAL PROTECTIVE EQUIPMENT REQUIREMENTS FOR GENERAL LABORATORY OPERATIONS |  |  | 
Hazard | Personal Protective Equipment Required |  | 
 | Eye | Face | Hand/Skin/Body
Any lab use of chemicals | Safety glasses at all times |  | Lab coat
Use of corrosive chemicals, strong oxidizing agents, | Chemical splash goggles | Full face shield and goggles (for work with | --Resistant gloves for chemical resistance of common glove
Carcinogens, mutagens, etc |  | Over 4 liters of corrosive liquid | Impervious lab coat, coveralls, apron, protective suit (for work with greater than 5 gallons of corrosive liquid)
Temperature Extremes |  |  | Insulated gloves for handling ovens, furnaces, cryogenic bath and other devices over 100 degrees Centigrade or below -1 degrees Centigrade
Sharp Objects (broken glass, rods into stoppers) |  |  | Heavy cloth barrier or leather gloves

## Slide 33: PPE
Respiratory Protection –The use of some substances may require the use of respiratory protection (respirators). See “Controlling Chemical Exposures” in this training for more information.

## Slide 34: Good Laboratory Practices
Personal Use of Chemicals –Lab workers are not allowed to remove chemicals from the lab for personal use.
Personal Hygiene –Hands should be washed frequently throughout the day, before leaving the lab, after contact with any hazardous materials, and before eating.

## Slide 35: Hazardous Material Handling and Storage

## Slide 36: Hazardous Material Handling and Storage
Hazards associated with various chemicals and gases vary widely. Understanding the hazards associated with a compound and minimizing the quantity used and stored in the lab will decrease chance of injury.

## Slide 37: Chemical Spills and Accident Response
As a matter of policy, University personnel should handle their own small spills and releases. For emergency situations i.e., large spills and leaks, evacuate and call 911 (Campus Police) from a safe location. See flow chart, Planning for Emergencies for more information.

## Slide 38: Chemical Storage
Chemicals ideally should be stored by compatibility, not simply by alphabetical arrangement. Oxidizers should be separated from organics, air/water reactives must be kept dry and cyanides should be stored away from acids.
Volatile toxic substances must be stored in volatile storage cabinets adequate to the purpose. When volatiles must be stored in a cooled atmosphere, explosion-proof refrigerators or similar specially designed equipment must be used.

## Slide 39: Examples of incompatible Chemicals
Acetic acid with Nitric acid
Bleach and Hydrochloric acid

## Slide 40: More Examples
Potassium dichromate, acetone and perchloric acid
Sodium borohydride and tetrodotoxin

## Slide 41: Flammables in Refrigerators
Do not store flammable liquids in a refrigerator unless it is approved for such storage. Such Refrigerators are designed not to spark inside the refrigerator. If refrigerated storage is needed, it is advisable to choose an explosion-proof refrigerator or flammable safe refrigerator. The differences in refrigerators are explained here.

## Slide 42: Chemical Handling
Chemical Handling –Encourage the use of poly coated bottles or use bottle carriers for transporting chemicals which are in regular glass containers. Close caps securely and avoid storing chemicals containers in hard to reach areas. Pour chemicals carefully, and never add water to concentrated acid. Metal containers and non-conductive containers (e.g., glass or plastic) holding more than five gallons must be grounded when transferring flammable liquids

## Slide 43: Cylinder Storage
Cylinders must be stored in well ventilated areas with their protective caps screwed on and the cylinder secured (e.g., strapped or chained in an upright position) to reduce the chance of the cylinder being knocked over.
  Do not store cylinders near heat or high traffic areas.
  Whenever possible do not store flammables and oxidizers together.
  Do not store empty and full cylinders together.
  Clearly mark empty cylinders.
  Storage of large quantities of cylinders must be done in an approved gas cylinder storage area.
  For storage and use of flammable gas cylinders, consult Office of Fire Marshal 257-6362.

## Slide 44: Labels
All chemical containers must be labeled.
All labels must be legible, in English and include chemical/product name (chemical formulas alone are not acceptable) and include information related to relevant hazards.
Labels on incoming containers must not be removed or defaced.
Date all peroxidizable and other chemicals, which may become unstable over time (e.g. picric acid, ethers); test and/or dispose of them when appropriate.
Waste chemical containers must be clearly marked as “Hazardous Waste” indicating specific names of waste chemicals.

## Slide 45: GHS Labels
The Globally Harmonized System of Classification and Labeling of Chemicals (GHS)
  GHS is an acronym for The Globally Harmonized System of Classification and Labeling of Chemicals. It is a common coherent approach to defining and classifying hazard, and communicating information on labels and safety data sheets. Its target audience includes workers, consumers, transport workers and emergency responders. It provides the underlying infrastructure for establishment of national, comprehensive chemical safety programs.

## Slide 46: GHS Labels
GHS Requirements
  Health, physical and environmental hazard criteria for substances and for classification of mixtures
  Provisions for communicating information on labels (including harmonized pictograms, hazard statements, and signals words)
  A 16- section safety data sheet – no longer called Material Safety Data Sheets

## Slide 47: GHS Labels
GHS Label Elements
  Symbol (hazard pictograms): convey health, physical and environmental hazard information, assigned to a GHS hazard class and category
  Signal Words: “Danger” or “Warning” are used to emphasize and indicate the relative level of severity of the hazard.
  Hazard Statements: Standard phrases assigned to a hazard class and category that describe the nature of the hazard.

## Slide 48: GHS Pictograms and Hazard Classes
Oxidizers | Flammables Self Reactives Pyrophorics Self-Heating Emits Flammable Gas Organic Peroxides | Explosives Self Reactives Organic Peroxides
Acute toxicity (severe) | Corrosives | Gases Under Pressure
Carcinogen Respiratory Sensitizer Reproductive Toxicity Target Organ Toxicity Mutagenicity Aspiration Toxicity | Environmental Toxicity | Irritant Dermal Sensitizer Acute toxicity (harmful) Narcotic Effects Respiratory Tract Irritation

## Slide 49: GHS Example Label
ToxiFlam (Contains: XYZ) Danger! Toxic If Swallowed, Flammable Liquid and Vapor Do not eat, drink or use tobacco when using this product. Wash hands thoroughly after handling. Keep container tightly closed. Keep away from heat/sparks/open flame. - No smoking. Wear protective gloves and eye/face protection. Ground container and receiving equipment. Use explosion-proof electrical equipment. Take precautionary measures against static discharge. Use only non-sparking tools. Store in cool/well-ventilated place.
IF SWALLOWED: Immediately call a POISON CONTROL CENTER or doctor/physician. Rinse mouth. In case of fire, use water fog, dry chemical, CO2, or "alcohol" foam.
See Safety Data Sheet for further details regarding safe use of this product. MyCompany, MyStreet, MyTown NJ 00000, Tel: 444 999 9999

## Slide 50: Laboratory Door Signage Requirements
Room number
Department
Laboratory supervisor's name
Emergency contacts, including names, office location, and office and emergency telephone numbers
Special hazards/instructions (e.g. location of large quantities of flammables or the presence of a "local alarm" system).

## Slide 51: Controlling Chemical Exposures

## Slide 52: Controlling Chemical Exposures
The Lab Standard requires the employer to determine and implement control measures to reduce employee exposure to hazardous chemicals; and particular attention must be given to the selection of control measures for chemicals that are known to be extremely hazardous. There are three major routes of entry for a chemical to enter the body: inhalation, absorption, and ingestion. Three types of controls for prevention of these various routes of entry include engineering controls, administrative or work practice controls and personal protective equipment. Each route of entry a chemical can take to enter the body can be controlled in a number of ways, as explained below.

## Slide 53: Inhalation Hazards
Most common route of exposure
Substitute to less volatile or toxic
Engineering control system
  Fume hoods
  Biosafety cabinet
  Glove box
  Closed system
Respirator may be used to reduce exposure

## Slide 54: Reducing Inhalation Hazards
Minimization of exposure time for individuals
Restrict access to an area where a hazardous chemical is used
Proper signage on lab door to indicate special hazards within.

## Slide 55: Respirators
OSHA Respiratory Standard (1910.134) must be followed for employees wearing a respirator
  Written respiratory program
  Training on proper use of respirators
  Medical surveillance
  Fit testing
  Contact Occupation Health and Safety (257-3827) for more information about using respirators in the laboratory.

## Slide 56: Skin/Eye Contact hazards
Wearing PPE to prevent contact hazards
Not all gloves are suited for all materials
If contact to a hazardous chemical occurs use the emergency eye wash or emergency safety shower.

## Slide 57: Emergency Eye Wash and Safety Shower
Safety showers and/ or eye washes are required in labs where corrosive chemicals are used. Eye washes must be tested weekly by laboratory personnel. Safety Showers must be tested monthly by building maintenance staff.

## Slide 58: Steps on using an Emergency Eye Wash
Always wash with tepid water or eye solution from the inside edges of the eyes to the outside; this will help to avoid washing the chemicals back into the eyes or into an unaffected eye.
Water or eye solution should not be directly aimed onto the eyeball, but aimed to the base of the nose
Flush eyes and eyelids with water or eye solution for a minimum of 15 minutes “Roll” eyes around to ensure full rinsing.
Immediately seek medical attention.

## Slide 59: Using a Safety Shower
Stand directly under the shower head
Pull handle to activate shower
Wash with tepid water for a minimum of 15 minutes
To turn off the shower push the handle up

## Slide 60: Ingestion Hazards
The Lab Standard forbids eating, drinking, applying make-up and lip balm in areas where hazardous chemicals are used.
Mouth pipetting is forbidden.
Always wear appropriate gloves.
Wash hands after using chemical and before eating.

## Slide 61: Exposure Assessment
At the request of faculty, staff or students, exposure evaluations may be conducted by Occupational Health for any suspected over exposure to substances regulated by OSHA. Records of exposure evaluations will be kept in the Occupational Health and Safety Department and provided to the department and affected employees and any other appropriate authorities at the University.

## Slide 62: Chemical Fume Hoods and Other Engineering Controls

## Slide 63: Face Velocities
Chemical fume hoods are the most common engineering control in laboratories. All chemical hoods at University of Kentucky facilities should have face velocities between 80-120 feet per minute (fpm)with the sash at a "working height" of approximately 12 inches. As a general rule, chemical hoods should not be operated with the sash fully open and should have the sash closed when not being used. The office of Occupational Health and Safety (OHS) will conduct a chemical hood inspection for all chemical hoods at the university. Chemical hoods with face velocities within the 80-150 fpm range may be used without restriction and will be marked with a fume hood sticker showing face velocity at a height designated with an arrow.

## Slide 64: Face Velocities
Face Velocity | Status | Use Restrictions
80-120 fpm | Passing | No Restrictions
121- 150 fpm | Marginal | No Restrictions
60-79 fpm | Marginal | Limited use
Below 60 and above 150 fpm | Failing | Do not use hood
Notes: Sash height is usually 12 inches, but can be moved to 18 inches.

## Slide 65: Fume Hoods Needing Repairs
If outside acceptable range, OHS will mark as failing and will tape the fume hoods sash closed with the red sticker.
OHS will submit a work order to repair fume hood.
OHS will re-evaluate fume hood once repaired.

## Slide 66: Safe Work Practices for Laboratory Fume Hoods
When using a chemical fume hood, one must remember that the hood does not provide absolute containment or absolute protection from the materials in the hood. That may be especially true for toxic airborne contaminants with exposure limits in the low part per billion ranges. However, for most exposures, a properly designed fume hood is a properly designed room can proved adequate protection by following certain work practices. The work practices below are recommended by the American Conference of Governmental Industrial Hygienists in their test: “Industrial Ventilation: A Manual of Recommended Practices.”

## Slide 67: Safe Work Practices for Laboratory Fume Hoods
All operations that may generate air contaminants at levels above the exposure limit must be conducted inside a fume hood.
Keep all apparatus at least 6 inches back from the face of the hood.
Do not put your head in the fume hood except for set up. Chemicals should not be in the fume hood at this time.
Do not use the fume hood as a waste disposal mechanism except for very small quantities of volatile materials.

## Slide 68: Work Practices Continued
Excessive storage of chemical or any apparatus in the hood will impair the performance of the chemical fume hood. Store flammable chemicals in an approved flammable storage cabinet. Store corrosive chemicals in a corrosive storage cabinet.
Make sure the fume hood is “on” whenever the hood in in use. A chemwipe is a visual indication of flow.
Be familiar with your chemical hood monitor and/or alarm

## Slide 69: Work Practices Continued
Using hazardous solids (powders) in the fume hood may not be appropriate.
Keep the slots in the hood baffle free of obstruction by apparatus or containers. No more than 25% of the bottom slot should be blocked.
Minimize foot traffic past the face of the fume hood.
Sash movement also creates some turbulence

## Slide 70: More Work Practices
Keep laboratory doors and windows closed (exception: some laboratories are designed for the lab doors to be open).
Do not remove fume hood sash or panels except when necessary for apparatus set-up; replace sash or panels before operating.
Do not place electrical receptacles or other spark sources inside the hood when flammable liquids or gases are present. No permanent electrical receptacles are permitted in the hood.

## Slide 71: More Work Practices
Use and appropriate barricade if there is a chance of explosion or eruption.
If the fume hood sash is supposed to be partially closed for operation, the fume hood should be so labeled and the appropriate closure point clearly indicated.
All chemical fume hoods should have spill protection lips (at the front of the hood and for cup sinks located in the hood.

## Slide 72: Even More Work Practices
Where perchloric acid is heated above ambient temperature, vapors may condense within the exhaust system to form explosive perchlorate salts. In such instances, specially designed chemical fume hood exhaust systems must be utilized. These systems will have dedicated exhaust and a water wash down system, and may be used for perchloric acid digestion only
Always use a special perchloric acid hood when heating
perchloric acid.

## Slide 73: Fume Hood Guide
Any questions or requests for assistance in evaluation of chemical fume hoods may be directed to Occupational Health and Safety at 257-3827
Guide to Fume Hood Flow Monitors

## Slide 74: Employee Information and Training
All individuals who work in laboratories who may be expose to hazardous chemicals must be apprised of the hazards of chemicals present in their work area.
THIS INFORMATION AND TRAINING AS OUTLINED BELOW MUST BE PROVIDED BEFORE INITIAL ASSIGNMENT AND BEFORE NEW EXPOSURE SITUATIONS.
Equipment necessary for the safe handling of hazardous substances must also be provided.
IT IS THE RESPONSIBILITY OF THE PRINCIPAL INVESTIGATOR TO ENSURE THAT ALL LABORATORY WORKERS HAVE BEEN PROPERLY TRAINED.
Occupational Health and Safety Department personnel will give presentations concerning general lab safety practices several times a year. However, training specific for the particular lab where an employee is assigned is the responsibility of that employee's supervisor.

## Slide 75: Mandatory Information Requirements
"Occupational Exposures to Hazardous Chemicals in Laboratories" (the OSHA Lab Standard -See Appendix I)
Chemical Hygiene Plan
Reference materials on chemical safety (including safety data sheets)
Permissible exposure limits for OSHA regulated substances
No applicable OSHA standard, the recommended exposure limits or threshold limit value (TLV) may be provided. Contact Occupational Health and Safety at 257-3827 for assistance
Signs and symptoms associated with exposure to the hazardous chemicals found in the lab

## Slide 76: Mandatory Training Requirements
Laboratory Worker training must include:
How a release of a hazardous chemicals is going to be detected. Examples of detection methods include visual appearance, odor, detector papers, and an understanding of chemical monitoring devices
Physical and health hazards of the chemicals
Hazardous waste training
The work practices, personal protective equipment, and emergency procedures to be used to ensure that the employee protects himself/herself from overexposure to hazardous chemicals
Medical consultations and examinations.
Notes: The manufacturer's safety data sheets (SDSs) will generally contain much of the above information needed to comply with the information and training requirements of the OSHA Lab Standard. Laboratory supervisors and employees should understand the relevant SDSs and/or other comparable literature on the hazardous chemicals which are used or stored in their laboratory. Additional training for specific lab hazards must be provided by the employee's supervisor.

## Slide 77: Prior Approval
The responsibility for approval of the acquisition and use of toxic chemical agents rests with the laboratory supervisor. Some materials including toxic compressed gases, radioactive materials, and certain recombinant DNA and biohazards require prior internal (University of Kentucky) or external approval at various levels. If there are questions concerning the need for approvals, appropriate Environmental Health and Safety departments (e.g. Radiation Safety) should be consulted.

## Slide 78: Medical Consultation
If an employee develops any symptoms thought to arise from chemical overexposure
After an event such as a major spill, leak or explosion which may have resulted in an overexposure
The departmental or Institutional Chemical Hygiene Officer identifies an overexposure as the result of an evaluation

## Slide 79: Medical Consultation
Employee accidents, injuries, or illnesses should be reported immediately by the employee’s supervisor. Student workers receiving pay other than scholarships, fellowships, student loans, or grants are generally considered employees. Any employee accident, injury, or illness must be reported by the supervisor to UK Workers’ Care by calling 1-800-440-6285.
Also the accident, injury or illness should be reported internally using the University’s Form 6.

## Slide 80: Chemical Hygiene Officer
The laboratory supervisor shall serve as the "Chemical Hygiene Officer" for her/his laboratories. The designated Chemical Hygiene Officer has the primary responsibility for safety and health within her/his laboratories. The Chemical Hygiene Officer is also responsible for conducting an annual review of the Chemical Hygiene Plan(s) that apply to his/her laboratories.
The Laboratory Safety Specialist of the Occupational Health and Safety Department is designated as the "Institutional Chemical Hygiene Officer" for the University of Kentucky. The Institutional Chemical Hygiene Officer is responsible for coordinating an annual review of the Model Chemical Hygiene Plan and serving as a resource to the individual laboratory Chemical Hygiene Officers.

## Slide 81: Pregnant Laboratory Workers
Individuals or childbearing potential are warned to be especially cautious when working with chemicals known to reproductive toxins. Some examples of these chemicals are arsenic, benzene, cadmium compounds, mercury compounds, and toluene, and formamide. These individuals must use appropriate protective apparel (especially gloves) to prevent skin contact. For more information and a complete list of reproductive toxins, please see here

## Slide 82: Special Provisions for Select Carcinogens, Reproductive Toxins and Toxic Chemicals
Provisions for additional employee protection for work with particularly hazardous substances. These include "select carcinogens," (see Appendix VII for a list of select carcinogens) reproductive toxins and substances that have a high degree of acute toxicity. The following provisions must be included:
  Establishment of a designated area;
  Use of containment devices such as fume hoods or glove boxes;
  Procedures for safe removal of contaminated waste; and
  Decontamination procedures.

## Slide 83: Special Provisions for Select Carcinogens, Reproductive Toxins and Toxic Chemicals – Minimum Guidelines
Quantities of these chemical used and stored in the laboratory must be minimized, as should their concentration in solution or mixtures.
Compressed gas cylinders which contain acutely toxic chemicals such as arsine, chlorine and nitrogen dioxide, must be kept in well-ventilated areas.
Detection equipment may be required in laboratories where chemicals, especially poisonous gases, with a high degree of acute toxicity are utilized.

## Slide 84: Special Provisions for Select Carcinogens, Reproductive Toxins and Toxic Chemicals – Minimum Guidelines
Work with genotoxins, reproductive toxins and acutely toxic chemicals must be performed within a certified functioning fume hood, biological safety cabinet, ventilated glove box, sealed system, or other systems designed to minimize exposure to the substances. (The exhaust air from the ventilation systems may require scrubbing, or other treatment, before being released into the atmosphere.) In all cases, work with these types of chemicals must be done in such a manner that the OSHA permissible exposure limits or similar standards are not exceeded.

## Slide 85: Special Provisions for Select Carcinogens, Reproductive Toxins and Toxic Chemicals – Minimum Guidelines
The ventilation efficiency of the designated fume hood, glove box or gas cabinet, and the operational effectiveness of mechanical and electrical equipment used to contain or manipulate these special substances should be evaluated periodically by the laboratory personnel at intervals determined by the Laboratory Supervisor. The interval of evaluating systems may vary from weekly to annually depending upon the frequency of usage, quantities employed and level of hazard.

## Slide 86: Special Provisions for Select Carcinogens, Reproductive Toxins and Toxic Chemicals – Minimum Guidelines
Each laboratory utilizing these substance must designate an area for this purpose and must sign or mark this area with an appropriate hazard warning. The designated area may be an entire lab like BSL-3 and 4 Labs. The designated area can be a piece of equipment like a fume hood or a biosafety cabinet. The designated are should be marked with a DANGER, specific agent, AUTHORIZED PERSONNEL ONLY or comparable warning sign.

## Slide 87: Special Provisions for Select Carcinogens, Reproductive Toxins and Toxic Chemicals – Minimum Guidelines
All laboratory workers who work in a laboratory, which has an designated area, must be trained on the following.
  Deleterious effects
  Signs and symptoms
  Safe handling and storage
  This training is the responsibility of the Laboratory Supervisor or PI and must be done prior to the use of any of these materials.

## Slide 88: Special Provisions for Select Carcinogens, Reproductive Toxins and Toxic Chemicals – Minimum Guidelines
Laboratory workers working with these chemicals must have access to appropriate protective equipment and clothing (available at no expense to the workers) and must be trained on how to properly utilize the safety equipment.
Special precautions to avoid release and exposure to highly toxic materials must be utilized.
  Volatile substance – kept cool
  Gases – properly functioning valves and regulators
  Dispersive solids – kept in closed containers, minimal air movement when used, and avoid static charges

## Slide 89: Special Provisions for Select Carcinogens, Reproductive Toxins and Toxic Chemicals – Minimum Guidelines
The designate working area must be thoroughly and appropriately decontaminated and cleaned at regular intervals determined by the Laboratory Supervisor. The interval may be as short as one day or as long as six months depending upon the frequency of usage and level of hazard.
For special disposal information, contact Environmental Management at 323-6280.

## Slide 90: Questions about Materials?
Jan Eggum
Phone: 257-3242
Email: jghamo2@email.uky.edu